Name___________________________		Hour _____	Date______________

Band Saw Safety Test

Directions: Select the answer that best completes the statement.  Place the letter of that answer in the blank.

____	1. You should wear eye protection ________________ are using the machine.

A. only when you			B. whenever you or someone else

C.  whenever you feel like it and 	D. only when you are reminded and

____	2.  Remove scrape pieces of wood from the band saw table when the

A.  machine is running		B.  the blade is coasting to a stop

C.  blade is completely stopped.	D.  All the above are safe and okay to do.

____	3. The upper guide and guard should be ________________ the material you are cutting.

A.  below the height of		B.  a ¼” or less above

C.  3/8” or less above			D.  ½” or less above

____	4.  Round material (wooden dowels or cylinders) can safely be cut on the band saw

A.  with nothing else to help.		B.  with a miter gauge.

C.  with the fence.			D.  with the use of a pliers or clamp.

____	5.  When cutting with the band saw, your hands should be _______________ the board.

A.  pushing from behind		B.  holding the front edges of

C.  off to the sides of			D. None of the above are okay.

____	6. If the band saw breaks

A.  get the teacher.			B.  shut off the machine.

C.  shut off the machine and get the teacher.	D.  just leave it for someone else to fix.

____	7.  Curves should be sawed

A.  very slowly.			B.  as fast as possible.

C.  with another machine, not the band saw.	D.  All of the above are okay.

_____	8.  Sharp curves and tight spots should be sawed

A.  very slowly			B.  as fast as possible.

C.  very slowly after making relief cuts.	D.  with another machine.

_____	9.  When you reach a spot where you must back up with the band saw you can back up

A.  when the machine is running.	B.  when the blade is completely stopped.

C.  when the blade is coating to a stop.	D.  never, only go forward.